## Slide 1: Gymtron
Mark Rumpel & Kyle Shaw
Advisor: Dr. Bais
The Automatic Weight Training Tracker

## Slide 2: Outline
Problem Statement
Objectives
Scope
System Overview (Block Diagram)
Demonstration Video
Design Choices
Challenges
Summary & Future Improvements

## Slide 3: Problem Statement
Gym goers want to track their progress
Manually tracking weight training is cumbersome
Solution: design a system that automatically tracks weight training sessions
Other applications include monitoring the participants of research studies that involve prescribing weight training regimens to a large group of people
Notes: https://www.indiegogo.com/projects/push-the-first-fitness-tracking-device-that-measures-strength

## Slide 4: Objectives
Provide seamless weight training tracking
  Allow users to log in to the device
  Record reps, sets, weight, & time
    i.e. measure distance/movement of the weight stack
  Provide simple visual feedback to confirm activity is being logged and provide guidance on proper form
  Display collected data on webpage

## Slide 5: Scope
Gymtron is targeted to new gym goers who may not have proper form and need guidance
  This is why a multi-purpose machine was chosen
  New users are able to view their progress
Demonstrate proof of concept using a single exercise given limited timeframe
Webserver is intended for very light traffic to reduce costs
  We disregarded scalability for this aspect of the project

## Slide 6: Block Diagram
Notes: Kyle

## Slide 7: User Experience

## Slide 8: Design Choices

## Slide 9: Processor
Looking for a cost-effective, flexible processor to handle data processing and serve web content
  Decided on the Raspberry Pi B+
For $40, we could use a single Raspberry Pi to both gather and process the data as well as host the webpage
Very well supported, many different devices are easily integrated together
Many libraries available
Built in graphical user interface (GUI)
http://www.raspberrypi.org/introducing-raspberry-pi-model-b-plus/

## Slide 10: Rep Tracking
Required to measure the position of weight stack
  Enough precision to ensure full range of movement
  Measure fast enough to ensure LED strip feedback is smooth
Chose ultrasonic distance sensor
  Bounces high frequency sound waves off objects in measurement range
  Cost effective and easy to install compared to other sensors that provide distance information
  15 – 20 degree measurement angle
Notes: Kyle
Measure stack 10 times per second with median filter with a size of three (25ms delay between distance measurements)

## Slide 11: Feedback
Provide simple visual feedback to confirm activity is being logged and provide guidance on proper form
RGB LED Strip
  Intuitive communication to user
  Simple to implement and control
Notes: With respect to the weight stack

## Slide 12: Weight Measurement
Determine which weight the user has selected from the weight stack
  Traditional scale difficult to implement and likely to sustain damage from weights
Indirectly measure the weight via a unique resistance supplied by each weight
Solution: Light Blue Bean (LBB)
  Bluetooth Low Energy module with microcontroller
  Analog input measures unique resistance of each weight
  Efficient battery use

## Slide 13: Login
Needed to identify user with little to no additional effort
Chose ITEAD NFC device
  Allowed users to sign in with a single swipe of gym card
  Users are already likely carrying their gym card already

## Slide 14: User Interface
Provide user with method to indicate the current set is complete
Button on the front panel for easy logout
LED’s on front panel indicate login status
Timeout feature to both automatically increment the current set and logout the current user

## Slide 15: Webserver & Database
Used Raspberry Pi as the webserver
Needed to serve dynamic content via web browser
Needed to store all data in an easily accessible manner
Scripting allows any user to view personalized and dynamic content
Database allows storage of data, easily accessible through queries
Chose php for scripting and MySQL for the database
  php and MySQL are very popular on today’s internet

## Slide 16: Challenges
Found original design relied too much on user performing workout with perfect timing
  In addition to timing out, added buttons to indicate end of set and logout instead of relying on perfect timing
  Added LED’s to convey status to user
  Much more intuitive and simple for user
  Sacrificed speed for ease of use

## Slide 17: Challenges
Ultrasonic sensor data quality
  Errors in the distance measurement caused unreliable operation
  Analyzed data from the ultrasonic sensor in Excel
  Implemented a median filter to improve accuracy
Notes: Delay in control loop
Nice value, real-time scheduling algorithm (FIFO, RR), priority level
Become more informed about OS scheduling and recommended programming practices

## Slide 18: Summary
Automated weight training tracker that makes user data available via a web interface
Used ultrasonic sensor, RGB LED strip, NFC card reader, and Raspberry Pi
Seamless integration with current workout routines
Interest in using system to track participants of research studies

## Slide 19: Future Improvements
Implement a separate offsite server to store data
  Safer, faster, scalable
Use WiFi for data transfer
  Reduce cables present on machine
Add more exercises
Creation of customized user profiles and in-depth data analysis on webpage
  Can consider physical differences and preferences between users
Improved weight stack tracking

## Slide 20: Questions?

## Slide 21
http://www.dariennewsonline.com/news/article/Koko-FitClub-brings-the-computer-age-to-the-local-3623193.php